## Slide 1: Basic Introduction of Arduino
2016. 08. 30.
Jinhyuk Yim (jinhyuk@uns.ajou.ac.kr)
Eungkyu Lee (eungkyu@uns.ajou.ac.kr)

## Slide 2
IoT
Arduino
  What is Arduino?
  Capability
Installing Arduino IDE Tool
Arduino Programming
  Sketch
  Examples
Practice

## Slide 3: Internet of Things

## Slide 4: What is the IoT
IoT (Internet of Things)
  A network of uniquely identifiable “things” that communicate without human interaction using IP connectivity

## Slide 5: IoT’s Key components
The four key components for realization of the above IoT architecture

## Slide 6: IoT Platform
Why is it needed?
  The architecture should be easy to implement and manage in a common method

## Slide 7: Arduino

## Slide 8: What is Arduino?
Microcontroller board
  It contains on-board power supply, USB port to communicate with PC, and an Atmel microcontroller chip.
  It simplify the process of creating any control system by providing the standard board that can be programmed and connected to the system without the need to any sophisticated PCB design and implementation.
Open source hardware
  any one can get the details of its design and modify it or make his own one himself.

## Slide 9: Arduino
Hardware
Community
Development Environment

## Slide 10: Arduino boards
……
http://arduino.cc/en/Main/Products

## Slide 11: Arduino Uno – basic model

## Slide 12: Arduino Uno Specification

## Slide 13: What can we do?
Wi-Fi controlled LED X-Max Tree
Wi-Fi Candy Bowl Monitor
Wireless gardening with Arduino
SMS Texting Pet Food Dish
Wi-Fi controlled mobile robot

## Slide 14: Install & Setting the Arduino IDE Tool

## Slide 15: Download the IDE Tool
Go to http://www.arduino.org/downloads

## Slide 16: Install the IDE Tool
Please make sure that ‘Install USB drivers’ is checked
Then keep press ‘Next’ button

## Slide 17: Install the USB Driver
When the Arduino IDE tool is installed in your PC, it will automatically install the USB driver for Arduino
Now you are ready to make an Arduino program

## Slide 18: Arduino Programming

## Slide 19: Procedure of Arduino Programming
3 steps to make your own Arduino program
  1. Make an Arduino source program using Arduino IDE tool
  2. Compile the source program
  3. Upload the source program to Arduino board

## Slide 20: Arduino Sketch
Global variables
  Declare variables at top
Setup()
  Initialize H/W, Run once at beginning
  pinMode() - set a pin as input or output
  Serial.Begin() - setup to terminal
Loop()
  Run repeatedly after setup
  digitalWrite() – set a digital pin high/low
  digitalRead() – read a digital pin’s state
  analogRead() – read an analog pin
  analogWrite() – write an analog PWM value
  delay() – wait an amount of time

## Slide 21: Arduino Main routine (main.cpp)
System initializatiONcode

## Slide 22: Arduino Sketch Example

## Slide 23: Practice

## Slide 24: Practice #1 – Basic LED control
Control the LED blink period
  Step 1: LED ON– 500ms, LED OFF – 500ms for 5 seconds
  Step 2: Then, LED ON– 250ms, LED OFF – 250ms for next 5 seconds
  Step 3: Then, LED ON– 125ms, LED OFF – 125ms for next 5 seconds
Hint: Use iteration statement (ex. while, for, etc.)

## Slide 25: Practice #2 – Control LED with Button (1/2)
Turn on the LED using Button
  Step 1: Connect the button to Arduino
    Connect Signal(S), Voltage(V), Ground(G) line

## Slide 26: Practice #2 – Control LED with Button (2/2)
Turn on the LED using Button
  Step 2: Turn on the LED when the button is pushed, and turn off the LED when the button is released