## Slide 1: Connecting Sensors to Arduino
2016. 09. 01.
Jinhyuk Yim (jinhyuk@uns.ajou.ac.kr)
Eungkyu Lee (eungkyu@uns.ajou.ac.kr)

## Slide 2
Arduino Sensors
  Sensor type
Sensor Programming
  Temperature and Humidity sensor
  PIR sensor
  Ultrasonic sensor
  Practice

## Slide 3: Arduino Sensors

## Slide 4: Various Sensors
Arduino can be utilized to connect a variety of sensors.
PIR sensor Module

## Slide 5: Sensor Type – Analog/Digital (1/2)
Sensors are usually classified into two – analog & digital
  Analog – infinite possibilities, continuous data (e.g., sound, smell, etc.)
  Digital – finite, discrete data (e.g., infrared, switch, button, etc.)
Analog Sensor | Digital Sensor
Light sensor | Switch
Sound sensor | Button
Pressure sensor | Infrared sensor

## Slide 6: Sensor Type – Analog/Digital (2/2)
However, some sensors operate in both way
  Accelerometer, temperature
Analog sensors have fixed data reading rate by the manufacturer
Users can configure data reading rate in digital sensors by using IC

## Slide 7: Sensor Type – Input/Output
Furthermore, we can classify the sensors into another way – Input & Output
  Input – switch, button, pressure, sound, etc.
  Output – LED, text LCD, etc.
Input Sensor | Output Sensor
Switch | LED
Button | Text LCD
Pressure sensor | Speaker

## Slide 8: Arduino sensor specification
Temperature and humidity sensor
  Low-cost digital temperature and humidity sensor
  20-80% humidity readings with ± 5% accuracy
  0-50 °C temperature readings ±2°C accuracy

## Slide 9: Arduino sensor specification
PIR sensor (Passive Infrared Sensor)
  Detection distance is 2cm~450cm
  High precision up to 3mm

## Slide 10: Arduino sensor specification
Ultrasonic sensor
  Distance range is 20mm~3500mm
  Serial baud rate is 9600

## Slide 11: Sensor Programming

## Slide 12: Temperature/Humidity Sensor
Checking temperature and humidity
  Step 1: Copy DHT11 folder to Arduino libraries folder
    C:\Users\ (AccountName) \Documents\Arduino\libraries
  Step 2: Import library
    Sketch -> Import library -> Add library
  Step 3: Connect the sensor to Arduino
    Voltage : 5v
  Step 4: Checking temperature and humidity
    Tools -> Serial Monitor
Ground
Voltage
Signal

## Slide 13: Temperature/Humidity Sensor Datasheet
Product Type : DHT11
Temperature Measurement Range : 20-90%RH
Humidity Measurement Range : 0-50 °C
Humidity Accuracy : ± 5% RH
Temperature Accuracy : ±2 °C
Body size : 15.5mm x 12mm x 5.5mm
Operating volt : 3 – 5v

## Slide 14: Code Example – Temperature/Humidity Sensor (1/2)
Functions for calculate a temperature and humidity
  Temperature
    Fahrenheit
      Fahrenheit is a temperature scale based on one proposed in 1724 by the physicist Daniel Gabriel Fahrenheit
    Kelvin
      The kelvin is a unit of measure for temperature based upon an absolute scale.
  Humidity
    Dew Point
      the temperature at which a given concentration of water vapor in air will form dew
    Dew Point Fast

## Slide 15: Code Example – Temperature/Humidity Sensor (2/2)

## Slide 16: PIR sensor (Passive Infrared Sensor)
Human body detection sensor
  It allow you to sense motion.
  Usually it used to detect whether a human has moved in or out of the sensors range.
How to use a PIR sensor
  Step 1: connect the sensor to Arduino
    Voltage : 5v
  Step 2: Checking detection result
    Tools -> Serial Monitor
Ground
Voltage
Signal

## Slide 17: PIR Sensor Datasheet
Product Type : Hc-SR501 Body Sensor Module
Operating Voltage Rage : 5-20VDC
Quiescent Current : < 50uA
Level output : High 3.3V/ Low 0V
Trigger : L can not be repeated trigger/H can be repeated trigger
Delay time : 5-300s Range
Block time : 2.5s
Board Dimensions : 32mm*24mm
Angle Sensor : <110 °C
Operation Temp : -15 - +70 degrees
Lens size sensor Diameter : 23mm

## Slide 18: Code Example - PIR Sensor
Detect a person using PIR
  Turn on the led during 1s when PIR sensor detects person

## Slide 19: Ultrasonic Sensor
How to use a Ultrasonic sensor
  Step 1: connect the sensor to Arduino
    Voltage : 5v
  Step 2: remove the cap in the backward
    It makes that ultrasonic sensor operating Echo/Trigger mode.
  Step 3: Turn on the Arduino
    Attention : you have to connect the sensor to Arduino
  Step 4: Checking detection result
    Tools -> Serial Monitor
Voltage
Echo
Trigger
GND
Echo/Trigger mode

## Slide 20: Ultrasonic Sensor Datasheet
Specifications
  Input voltage: 5V DC
  Quiescent current: less than 2mA
  Level output: 5V high
  Level output: at the end of 0V
  Induction angle: not more than 15 degrees
  Detection distance: 2cm - 450cm
  Precision: up to 1mm
  Dimensions: 4.4cm x 2.6cm x 1.4cm
  Weight: 43g

## Slide 21: Ultrasonic sensor Code example

## Slide 22: Practice

## Slide 23: Practice #1
Find a distance between ultrasonic sensor and you
  Step 1: Connect sensors to the bread board
  Step 2: When you click the button, detects a person using PIR sensor
  Step 3: When PIR sensor detects a person then shows distance between sensor and you

## Slide 24: Practice #2
Make a Sonar radar with ultrasonic and motor
  Servo motor  Tower Pro SG-5010
  https://www.arduino.cc/en/Tutorial/Sweep
  Rotate 360 degree left and right